## Slide 1
QUEST ARUCO AVATAR
Viewpoint drift: what was tested, what was found, and what it assumes
CAMERA
MARKERS
COMMON POSE
FILTER
AVATAR

## Slide 2
CURRENT QUEST RUNTIME
Why the avatar drifts on side and distant views — what was tested and found
SYMPTOM — viewed from the front the avatar sits on the mannequin. Step to the left or right, or stand further back, and it no longer lines up. The mannequin never moved, and once the placement locks the avatar's transform is never rewritten — so nothing actually moved. What changed is where the system BELIEVES the anchor is, and that belief depends on where you stand.
HOW IT WAS TESTED — the real fusion code (navel_provider.gd) was replayed offline, frame by frame, against labelled recordings in which the mannequin was stationary throughout. Any change between viewpoints is therefore error, not motion. Settings were chosen on three six-viewpoint stationary recordings (2026-09-03) and then scored once on three walked viewpoint recordings (2026-09-09) that were never used to choose anything — so a result that only fits the tuning data is visible as overfitting.
THE DECISIVE TEST — the walked recordings confound the two explanations, because "far left" is both far away AND to the side. The stationary recordings separate them: there the user stood still and only turned to look, holding range constant while angle changed.
RESULT: ANGLE, NOT DISTANCE — front 1.92 m is the reference. Left view at 1.94 m, only 3 cm farther, drifts 4.30 cm. Right view at 1.85 m, actually CLOSER, drifts 8.90 cm. And the farthest view of all, 2.24 m, has the SMALLEST drift at 3.09 cm. Distance does not predict viewpoint drift. In the walked set both matter: left 6.02 cm at 1.75 m rising to far-left 12.04 cm at 2.16 m — stepping aside costs immediately, going far compounds it.
NOISE IS NOT BIAS — this is the crux. Per-frame disagreement between the markers DOES grow strongly with range, from 24 mm under 0.8 m to 127 mm beyond 1.8 m (rho +0.57; viewing angle only +0.24), and 59% of it lies along the camera's view axis. But that is NOISE, and averaging removes it. The viewpoint shift is BIAS: it sits still while you stand still, so no amount of averaging can touch it.
WHAT WAS TRIED AND DID NOT WORK — range weighting (w = 1/range^k) measured 6.30 cm at k=0 falling only to 6.17 cm at k=3, about 2%. The 60 mm / 20° agreement gate scored WORSE than a plain average on held-out data (7.84 vs 7.49 cm) and ranked 34th of 168 in a grid search. Medoid, dead zones, smoothing and rest-pull all attack noise, which is why none of them helped.
WHY THE LOCK DOES NOT CURE IT — the lock freezes the avatar, so it genuinely cannot drift. But the lock is earned while standing at the FRONT, so it inherits the front viewpoint's bias. Step to the side and the avatar has not moved — the correct answer has.
CANDIDATE CAUSES, NOT YET ISOLATED — the three markers disagree by a median of 68.9 mm about where the anchor is, larger than the drift being chased. The stored marker geometry is wrong by 20–40 mm. The markers are 10 cm, small at 2 m. Camera intrinsics, distortion and the camera-to-headset transform are unvalidated. A left/right asymmetry appears in both data sets but with OPPOSITE sign, so it does not support an optics explanation.
What this cannot tell you: there is no physical ground truth in any of these recordings, so every figure is agreement with that recording's own front reference, not absolute accuracy — front reads 0.00 cm by definition, which is not evidence that front is correct. All of it is offline replay of pre-freeze recordings; none has been measured on the locked build. Next: recalibrate the marker geometry, use markers larger than 10 cm, then re-record and re-measure before touching fusion again.
tools/side_view_vs_range.py • tools/diagnose_marker_disagreement.py • tools/analyze_subsets_and_freeze.py • tools/tune_marker_agreement.py • results in builds/viewpoint_research/*.json

## Slide 3
CURRENT QUEST RUNTIME
Testing the fusion rule: does the agreement gate help?
WHAT A GATE IS — every visible marker carries its own calibration offset, so each one independently predicts the same anchor point. The gate is a pass/fail test applied before averaging: two predictions "agree" only if they lie within 60 mm AND 20° of each other. Only markers that agree are averaged together.
THREE BRANCHES per frame, counted on aruco_viewpoint_1788955119: all three agree and are averaged 28.9% • only one pair agrees, so the third marker is discarded 34.6% • no pair agrees, so the previous frame's answer is reused 22.6% • a single marker is visible with nothing to check it against 13.9%.
RESULT on recordings the tuning never saw: plain average 7.49 cm, gate at 60 mm / 20° 7.84 cm. The gate is slightly WORSE than having no gate. A 168-point grid search ranked 60/20 at 34th, and the combination that won on the tuning data scored worse on held-out data — so there is no better value to move to either.
WHY IT FAILS — agreement is not correctness. At the "right" viewpoint: ID0 alone 12.25 cm, gate 10.52 cm, plain average 2.45 cm. ID0 was badly wrong and the third marker would have corrected it, but the gate found a pair that agreed WITH EACH OTHER, discarded the marker that disagreed, and kept the error.
THE GATES WERE NEVER TUNED — 60 mm and 20° were read off the good-pair spread of one Front recording and rounded up; the code comment says exactly that. This grid search was the first time they were tested.
Scored as consistency: the mannequin never moved, so any shift between viewpoints is error. There is no physical ground truth in these recordings, so this measures agreement with each recording's own front reference, not absolute accuracy.
tools/tune_marker_agreement.py • tools/compare_id0_vs_fusion.py • builds/viewpoint_research/marker_agreement_grid.json

## Slide 4
CURRENT QUEST RUNTIME
How many markers to fuse, and when to stop trusting them
HOW MANY — scored only on frames where all three markers are visible, so every option sees identical frames. ID0+ID2 5.61 cm tune / 6.11 cm held-out • all three 6.41 / 6.52 • ID0 alone 5.79 / 8.00 • ID1 alone 9.30 / 8.97. Fusing TWO beats fusing three, and this is the only result of the day that held up on data it was not chosen from.
ID1 AND ID2 FAIL DIFFERENTLY — ID1 is biased: a moderate but consistent error, the worst of any marker on its own. ID2 is spiky: the odd one out in 47.9% of frames, with rotation-induced error reaching 187.8 mm at p90, but those errors average out. That is why ID0+ID2 beats ID0+ID1.
ID0 IS STRUCTURALLY SAFEST — its calibration offset is exactly zero, so it IS the anchor. It has no lever arm, marker rotation error cannot displace it at all, and it is the odd one out in only 12.0% of frames.
WHEN TO STOP TRUSTING A FRAME — residual = the largest gap between the visible predictions. Above about 40 mm, reject the frame and hold the last accepted pose instead of choosing a least-bad candidate. Held-out error improves from 7.49 to 7.17 cm, and a genuine mannequin relocation still survives (retention 1.02).
SCALE OF THE PROBLEM — the three markers disagree by a median of 68.9 mm about where the anchor is, which is larger than the 5–8 cm viewpoint drift being chased. The stored marker geometry is also wrong by 20–40 mm (ID0-ID1 19.7, ID0-ID2 30.6, ID1-ID2 40.3) — free accuracy available from a recalibration.
None of these changes are implemented. The runtime still fuses every visible marker through the 60 mm / 20° gate.
tools/analyze_subsets_and_freeze.py • tools/diagnose_marker_disagreement.py

## Slide 5
CURRENT QUEST RUNTIME
Side-view drift is viewing angle, not distance
THE CONFOUND — in the walked recordings "far left" is both far away AND to the side, so the two cannot be separated. The stationary recordings separate them: there the user stood still and only turned to look, so the side views sit at the same range as front.
SAME RANGE, STILL DRIFTS — front 1.92 m is the reference. Left view 1.94 m, only 3 cm farther, drifts 4.30 cm. Right view 1.85 m, actually closer, drifts 8.90 cm. And the farthest view of all at 2.24 m has the SMALLEST drift, 3.09 cm. Distance does not predict viewpoint drift.
NOISE VERSUS BIAS — per-frame marker disagreement does grow strongly with range, from 24 mm under 0.8 m to 127 mm past 1.8 m. That is noise, and averaging removes it. The viewpoint shift is bias: it stays put while you stand still, so no amount of averaging touches it.
RANGE WEIGHTING DOES NOT HELP — weighting each marker by 1/range^k was measured directly: mean drift 6.30 cm at k=0, falling only to 6.17 cm at k=3, and the right view does not improve at all.
NEAR AND FAR BOTH — walked: left 6.02 cm at 1.75 m, far left 12.04 cm at 2.16 m; right 2.10 cm at 1.83 m, far right 10.59 cm at 2.35 m. Stepping to the side costs immediately; going far compounds it.
CONSEQUENCE — the lock captures the pose from the front, so it inherits the front bias. Standing to the side, the avatar has not moved but the correct answer has. This is why filtering, medoids, dead zones, smoothing and fusion weighting have all failed to fix it: every one of them attacks noise.
Cause not yet isolated. A left/right asymmetry appears in both data sets but with opposite sign, so it does not support an intrinsics or extrinsics explanation. Recalibrating the marker geometry and using markers larger than 10 cm are the two changes already measured as justified.
tools/side_view_vs_range.py • builds/viewpoint_research/side_view_vs_range.json

## Slide 6
CURRENT QUEST RUNTIME
Assumptions the analysis rests on, and what it cannot show
STATIONARY MANNEQUIN — every number assumes the mannequin did not move during a recording, so that any change between viewpoints is error. This comes from the phase labels and the operator's report; it was not independently verified. If it did move, part of what is counted as error was real motion.
NO GROUND TRUTH — nothing here measures where the anchor physically is. Every figure is agreement with that recording's OWN front median. Front reads 0.00 cm by construction, which is not evidence that front is correct: all viewpoints could be wrong together and this method would not reveal it.
CALIBRATION — the offsets used are project/default_navel_calibration.cfg. Checked against the headset's user://navel_calibration_20260905.cfg, which takes precedence at runtime: byte-identical, so the replay used the geometry the device actually uses.
REPLAY FIDELITY — the Python re-implementation of _fuse and _floor_lock reproduces the previously published metrics.json for the plain-mean build: left 5.81 vs 5.79, right 2.35 vs 2.41, far-left 13.63 vs 13.71 cm. far-front and far-right agree less well (9.84 vs 8.92, 15.30 vs 11.46), most likely different missing-row handling — treat those two as less certain.
PRE-FREEZE DATA ONLY — every recording analysed predates the placement lock. Nothing here is measured on the locked build. The two sessions recorded from it carry only a "front" label, so no viewpoint comparison is possible from them.
SAMPLE SIZE — 3 stationary recordings to choose settings, 3 walked recordings held out for validation, 3 moving recordings as the movement guard. That is thin. A result that survives the held-out set deserves more trust than one that does not; neither is proof.
WINDOWING — the first second of every phase is discarded and a phase needs at least 5 remaining samples. Frames showing fewer than two markers cannot be cross-checked at all, and that is 13.9% of frames.
INTRINSICS — the radial test uses the hardcoded values from main_3d.gd (fx 438.5, fy 439.2, cx 322.7, cy 321.1 after the 0.5 downscale), the same ones the runtime uses. Marker CENTRE radius is used as a proxy, although distortion actually acts on the corners.
NO CODE WAS CHANGED — all of this is offline replay against recorded CSVs. The runtime still applies the 60 mm / 20° gate, still fuses every visible marker, and has no freeze rule. Nothing recommended here has been implemented.
The single biggest limitation is the absence of ground truth. Consistency between viewpoints can be measured without it, but accuracy cannot. Physical measurement of the anchor position, or an independent tracker, is what would turn these into accuracy claims.
Assumptions verified where possible: calibration compared against the device copy; replay validated against builds/viewpoint_research/metrics.json

## Slide 7
CURRENT QUEST RUNTIME
Everything that was tried — including what failed
HELD UP ON HELD-OUT DATA — subset comparison across all seven combinations of the three markers, scored only on frames where all three are visible: ID0+ID2 beats all three (6.11 vs 6.52 cm). • Separating viewing angle from range using the stationary recordings: angle, not distance. • Rejecting a frame when the markers disagree by more than about 40 mm and holding the last pose: 7.49 to 7.17 cm, modest but real.
DID NOT WORK — a 168-point grid search over the agreement gates: the winner (250 mm / 12°) scored WORSE on held-out data than the setting it replaced, and the gate itself loses to a plain average (7.84 vs 7.49 cm). • Range weighting w = 1/range^k for k = 0 to 3: 6.30 to 6.17 cm, about 2%. • Using ID0 alone with no fusion: worse than fusing on both mean and worst case, and ID0 is only visible in 70% of frames.
DIAGNOSTICS RUN — branch-frequency count of _fuse (28.9 / 34.6 / 22.6 / 13.9%). • Odd-one-out attribution per marker (ID0 12.0%, ID1 40.1%, ID2 47.9%). • Calibration geometry check comparing observed marker-to-marker pose against the stored offsets: 20–40 mm systematic bias. • Rotation-share decomposition through each marker's lever arm. • Depth versus lateral split in the camera frame: 59% along the view axis. • Range and obliquity correlation: +0.57 and +0.24. • Radial image distance against residual: −0.14 raw, +0.31 once range is held constant.
RAISED AND THEN WITHDRAWN — rotation error acting through the lever arm: refuted, because ID0's offset is exactly zero so rotation cannot displace it, and the stationary test that EXCLUDES rotation still drifts. • "Place and lock from close range": refuted, because at equal range the side views still drift and the farthest view drifts least. • Uncorrected lens distortion: corrected, the active pipeline does apply distortion coefficients; the zeroed vectors are in unused picture/webcam code paths. • A left/right asymmetry as an optics clue: withdrawn, the asymmetry has opposite sign in the two data sets.
STILL OPEN — the device's own intrinsics and distortion are read from ACAMERA_LENS_INTRINSIC_CALIBRATION and ACAMERA_LENS_DISTORTION, then discarded: the per-camera selection is commented out and a rescale from 1280×1280 to the working resolution is unfinished. Whether using them changes anything is untested.
Reported in the order the work happened, failures included, because a method that was tried and rejected is part of the evidence. Four hypotheses were raised and then withdrawn when the data or the code contradicted them.
tools/compare_id0_vs_fusion.py • tune_marker_agreement.py • analyze_subsets_and_freeze.py • diagnose_marker_disagreement.py • side_view_vs_range.py • test_distortion_hypothesis.py

## Slide 8
DRIFT FIX — 22 SEPTEMBER 2026
The drift was a range error: found from the recordings, fixed by one factor
OBSERVATION — correct from the front, slid sideways from the sides, moved away from the viewer at distance.
ASSUMPTION — the mannequin does not move during a recording, so one marker must land on one spot in the room from every viewpoint.
DATA — 7 recorded walks (3 and 9 September), 3 markers each = 21 independent fits.
METHOD — per view: position in room = head position + s × (marker offset from camera). Unknowns: the true spot X and one scale s. Least squares over all views; X is the mean, s has a closed form. No external reference value is needed.
RESULT — s = 0.937 in every session (common marker 0.932–0.940; all 21 fits average 0.937). Every distance was measured ~6.7 % too long. Error along the line of sight, lateral ~1 cm → range, not lens distortion.
FIX — camera focal length × 0.937 (877.1 → 821.8, 878.3 → 823.0). One number, applies to all markers, independent of marker placement.
VERIFIED — two new recordings (15 September) fit s = 1.000, 0.990, 1.005. Side-view error 6–12 cm → ~3 cm.
What the data cannot decide: a focal-length error and a headset tracking-scale error produce the same picture in the app. A tripod tape test at 1 m and 2 m would separate them. Only matters if raw marker distances are used for something else.
tools/depth_scale_fit.py — recordings aruco_stationary_17884* (3 Sep), aruco_viewpoint_17889* (9 Sep), aruco_viewpoint_17894* (15 Sep, verification)
8

## Slide 9
DRIFT FIX — 22 SEPTEMBER 2026
What remained after the scale fix, and what was done about it
RESIDUAL RANGE — beyond 1.2 m the distance still read too long, by 6.4 % of the extra distance (both sessions, common and navel agree). Corrected per marker before placement; common and navel within 1 cm out to 2.2 m.
MIRROR POSES — from the side the detector sometimes returns the flipped solution of a flat marker: 30–40° turned, 12–14 cm off (33 % of left-view samples for the common marker, 86 % of right-view samples for the chest). Rejected when the marker face points > 45° from up; its last good pose stands in for up to 1 s. Removed the turning and the jumps.
RE-ANCHOR — thresholds raised to 8 cm / 8° so viewpoint bias is not mistaken for the mannequin being moved.
OPEN — beyond 2 m the chest marker keeps a steeper error the model does not cover. Next accuracy step: one pose from all 12 marker corners in the detector (C++ side).
NOT THE APP — the headset has been tracking in low-light mode, relocalising ~once a minute; the per-frame trace shows the avatar steady to < 0.5 mm in the app's world while the user saw shaking.
Tried in replay and not shipped (< 1 cm gain or worse): weighting the common marker higher, a 10 cm outlier rule, a fresh calibration from the new recordings, a rigid-body consistency check between markers.
tools/viewpoint_phase_summary.py — tools/replay_summary.py — tests/replay_recording.gd — device log: adb logcat | grep endTransition[worldTracking]
9

## Slide 10
DRIFT FIX — 22 SEPTEMBER 2026
Why the mirror-pose test is needed even though the floor lock discards tilt
THE QUESTION — the floor lock already forces the avatar flat, so why not floor-lock first and skip the mirror test?
WHAT THE FLOOR LOCK DOES — reads one thing from the marker, its along-body axis, flattens it onto the floor and keeps that as the heading; overwrites the face direction with the room's down; copies the position through untouched. It never inspects the sample, so it cannot reject one.
WHAT A MIRRORED SAMPLE IS WRONG ABOUT — three things at once: face pointing sideways (85–95° from up instead of 5–25°), heading turned 30–40° on the floor, position shifted 12–14 cm. From the side the picture fits both candidates, so the detector's pick is a coin toss.
MIRRORED SAMPLE THROUGH THE FLOOR LOCK — turned heading flattened and taken as truth; shifted position copied through; sideways face overwritten and gone. Output: a clean, flat, confident, wrong pose. Fused with the good ones, the avatar's feet swing ~60 cm for a 35° turn, pivoting about the chest marker.
MIRRORED SAMPLE THROUGH THE TEST — the test reads the face direction, the one thing the floor lock throws away. Sideways → the whole sample is dropped, wrong heading and wrong position with it; the marker's last good pose stands in for up to 1 s. Only surviving samples are fused and then floor-locked.
FLOOR LOCK EARLIER — every sample would reach the test already flattened, face direction = down, angle 0°: the test would pass everything, including the mirrors. Same as having no test.
Rule: the face direction must be read before it is discarded. The order is not the point; the check could live inside the floor lock, but it would be the same test. The two angles are different: the 45° threshold is on tilt (face vs up), the 30–40° is the heading error that goes away with the rejected sample and is never measured at run time. Removing the mirror at the source (choose the candidate facing up, or fix each marker's known tilt in the solve) needs the corners, which only the C++ detector has.
navel_provider.gd: _is_flipped (before fusion) — _floor_lock (after fusion); tools/viewpoint_phase_summary.py for the 30–40° / 12–14 cm figures
10

## Slide 11
DRIFT FIX — 22 SEPTEMBER 2026
Re-anchor threshold 8 cm / 8°: why it is tied to the viewpoint error, and how it was set
WHAT RE-ANCHOR WATCHES FOR — the filter holds a rest pose and re-anchors when the incoming measurement settles at a new spot and stays there, steady, over several detections. That pattern is its definition of "the mannequin was moved".
WHY THE VIEWPOINT ERROR MATTERS — the filter never sees the mannequin, only the detector's numbers. Walk to the side and stop: the markers read ~5 cm off, steadily, for as long as you stand there. A stable measurement somewhere else: exactly the pattern above. A real move and a viewpoint error are indistinguishable to it.
SO THE THRESHOLD IS A SIZE TEST — it must sit above the largest false alarm the test can receive, and the viewpoint error is that false alarm. Below it, walking round the mannequin re-anchors it: on the headset (15 Sep, floors 4 cm / 3°) the avatar crept toward the far viewer and turned a few degrees "at times", and jumped back on returning to the front.
HOW 8 / 8 WAS SET — bracketed, not fitted. Lower bound: residual viewpoint bias after the fx fix, ~4–6 cm and a few degrees (15 Sep recordings). Upper bound: real moves in the recorded tests, 105–300 mm and tens of degrees. 8 cm / 8° is ~1.5–2× the bias and well under the smallest real move; no data separates 8 from 7 or 10.
WHAT IT COSTS — a real move under 8 cm / 8° is not followed: the avatar stays put, off by that amount, until the mannequin moves further or is re-placed by nudge.
HOW TO LOWER IT — give the filter the cause, not just the size: the marker error changes only while the head moves, the mannequin at any time. Viewer-motion gate (built 16 Sep, in replay OK, reverted with the CPR rollback): hold while the head moves; once still 0.5 s, average 5 readings; ≤ 6 cm / 6° is bias and is subtracted, more is a move and is followed; > 15 cm / 15° on 3 detections is followed at once; no small-move verdict beyond 1.8 m. Floor could then drop to 3–4 cm.
Not a fix: enlarging the avatar to hide a few centimetres. The CPR hand target on the chest needs centimetre placement, and +5 % already looked too wide on video. The range correction has since cut the far-view bias to ~3–4 cm, so the floor could come down a little even without the gate; no evidence yet that it needs to.
avatar_rig_navel.gd: REANCHOR_MIN_POSITION_M / REANCHOR_MIN_ROTATION_DEG (commit a3efe0d); viewer gate: commit 105af97 (_gate_measurement)
11