## Slide 1
QUEST ARUCO AVATAR
How the avatar is placed on the mannequin
Floor-locked, grid-selected runtime • installed 5 September 2026
CAMERA
MARKERS
COMMON POSE
FILTER
AVATAR

## Slide 2
CURRENT QUEST RUNTIME
The placement problem
Three physical markers must describe one virtual body anchor.
ID0 common
ID1 chest
ID2 torso
ONE COMMON 6-DoF POSE
Pose = position (X,Y,Z) + orientation
The calibration stores a full marker → common transform, including both translation and rotation.
marker world pose × marker-to-common offset = common estimate
navel_provider.gd • default_navel_calibration.cfg
2

## Slide 3
CURRENT QUEST RUNTIME
Reconstruct, fuse and floor-lock the common pose
Only markers from the exact newest camera result are combined; orientation is then constrained to the floor.
1 marker
Use its reconstructed common pose
2 markers
Mean position + sign-aligned quaternion average
3 markers
Mean position + sign-aligned quaternion average (same as 2)
navel_provider.gd::_fuse • navel_provider.gd::_floor_lock
4
FLOOR-LOCK
Marker local Y → horizontal body direction
Quest UP → vertical reference
Cross product → sideways axis
Marker pitch + roll discarded

## Slide 4
CURRENT QUEST RUNTIME
Startup: learn a robust session rest pose
The avatar stays hidden while independent fused poses are collected.
30
E0
33
E1
36
E2
39
E3
Each estimate uses coordinate-median position + one measured rotation medoid over all collected poses.
Stable comparison Δ position ≤ 1.5 mm AND Δ rotation ≤ 1.0°
4 stable comparisons → detection 42 earliest Detection 100 fallback ≈ 10 s at 10 Hz
Grid-selected on the 2026-09-04 session • ≥95% stationary confirmation • ≤5% moving false acceptance
5

## Slide 5
CURRENT QUEST RUNTIME
After startup: the runtime filter
1
FLOOR-LOCKED MEASUREMENT
2
5-POSE MEDOID
3
DEAD ZONES
4
EXPONENTIAL SMOOTHING
5
LOCAL REST PULL
Updates once per new OpenCV timestamp,
Rejects a lone temporal outlier
Holds tiny position / rotation changes
Moves continuously
Always active;
Selected values: window 5 • radius 0.20 m • position dead zone 20 mm • rotation dead zone 0.3° • smoothing τ = 1.2 s • prior τ = 2 s • rest re-anchor beyond 40 mm / 3°
simple_pose_stabilizer.gd • avatar_rig_navel.gd
6

## Slide 6
CURRENT QUEST RUNTIME
Why the five-pose medoid rejects jumps
M1
M2
M3
chosen
M5
M6
bad
Six measurements agree; one is far away. The medoid chooses the actual measured pose with the smallest total distance to all others.
score = position distance + radius × rotation angle
Selected radius = 0.20 m At this radius, 1° rotation contributes approximately the same score as 3.5 mm of position error.
simple_pose_stabilizer.gd::_medoid • 0.20 m selected on the 2026-09-04 session replays
7

## Slide 7
CURRENT QUEST RUNTIME
Dead zone, smoothing and prior do different jobs
DEAD ZONE
≤20 mm position ≤0.3° rotation Hold the corresponding output channel.
SMOOTHING
τ = 1.2 s 63% after 1.2 s 95% after 3.6 s
REST PRIOR
τ = 2 s Always active; after a re-anchor the landing rule closes onto the new rest at smoothing speed.
A stable endpoint beyond 40 mm or 3° re-anchors the remembered rest itself, so the prior pulls toward the new location instead of dragging a relocated mannequin backwards.
Filtering order: medoid → dead zones → smoothing → weak rest pull • rest re-anchors at stable endpoints
8

## Slide 8
CURRENT QUEST RUNTIME
Two poses exist: displayed pose and remembered rest
Measurement-only 7-pose medoid
3-target window stationary?
Remembered rest re-anchors (jumps)
Re-anchor floor: 40 mm / 3°
Rest never learns from a single raw pose and never from the displayed pose, because that output already contains smoothing and prior feedback. It adopts the measurement-only medoid target once the complete 3-target window is stationary (≤1.5 mm / ≤1.0°) and clearly displaced from the old rest. Position and rotation re-anchor independently.
LIMIT: the newest stationary test exposed stable viewpoint errors up to 114 mm. The re-anchor floor cannot reject a large, stable wrong pose; marker agreement must be fixed before fusion.
navel_provider.gd::reanchor_rest_from_stable_target • simple_pose_stabilizer.gd::_update_stable_endpoint_state
9

## Slide 9
CURRENT QUEST RUNTIME
Tracking loss and Quest-menu resume
Temporary marker loss
No new marker result for 300 ms
Hide avatar keep last internal pose
Collect 7 fresh detections
App resumes after Quest menu
Old XR world rest may no longer be valid
Keep permanent marker offsets
Relearn startup rest 55–100 detections ≈11–20 s
marker_freshness.gd • avatar_rig_navel.gd::_notification
10

## Slide 10
CURRENT QUEST RUNTIME
Final render transform
FILTERED COMMON POSE
×
FIXED MODEL ALIGNMENT
=
VISIBLE AVATAR
Scale 0.77 Rotation −90° X (lay flat) Position (0.07256, −0.127499, 0.177248) m
Floor-lock sets local Z down and local Y to horizontal body heading before this fixed model correction is applied.
A persistent fixed offset here cannot be repaired by waiting, smoothing, the prior or 600-second healing.
main_3d.tscn: mannequin child transform • AvatarRig.global_transform = filtered pose
11

## Slide 11
CURRENT QUEST RUNTIME
What the latest experiments selected
Stationary + 617.5 mm movement replays selected the filter; hiding and compression recordings were hold-out checks.
Parameter group
Examples in grid
Current
Status
Startup convergence
start / step / fallback
30 / 3 / 100
Selected*
Display filter
window • radius • dead zones • smoothing
5 • 0.20 m • 20 mm / 0.3° • 1.2 s
Selected*
Prior and re-anchor
prior • re-anchor floor
2 s • 40 mm / 3°
Selected*
Fusion strategy
mean • robust • agreement-gated
mean for all
Open issue
Hold-out result: filtering cannot remove stable 2–12 cm disagreement between marker estimates
*Best supported values for this dataset; marker-fusion reliability remains unresolved
12

## Slide 12
CURRENT QUEST RUNTIME
How this prototype supports NaReT
NARET REQUIREMENT
German–Polish AI/XR learning through realistic resuscitation scenarios
QUEST PROTOTYPE
Place and stabilize the virtual patient on the real CPR mannequin
TECHNICAL METHOD
ArUco markers, calibration, pose fusion and filtering
Important: NaReT requires a reliable XR learning experience. It does not prescribe ArUco markers or a particular barcode size.
Project method: concept → prototype → testing → evaluation → iterative improvement
Sources: NaReT JEMS A1.5 • About the project / O projekcie
13

## Slide 13
CURRENT QUEST RUNTIME
What to do next — in the correct order
1
ARCHIVE INSTALLED BUILD
Keep the 5 September APK, exact filter values and previous calibration as the reproducible baseline.
2
FIX MARKER AGREEMENT
Detect disagreeing common-pose estimates before fusion; do not blindly mean-average a bad marker.
3
RE-CHECK CALIBRATION
Use tape-consistent marker geometry and test that changing headset viewpoint does not move the mannequin.
4
VALIDATE FULL CPR
Repeat hiding, compression and complete BLS scenarios after fusion is corrected.
The installed filter is the baseline; marker agreement is now the highest-priority tracking problem
14

## Slide 14
CURRENT QUEST RUNTIME
Small-marker experiment — change one thing at a time
10 cm
CONTROL
7.5 cm
FIRST CANDIDATE
5 cm
SMALLEST CANDIDATE
For every size
Print exact black-square size + clear white border
Set aruco_patch_size + recalibrate mounting
Record labelled CPR-view tests
Compare reliability and alignment
Measure: detection rate • longest loss • position/rotation wobble • alignment error • recovery
Keep dictionary, IDs, resolution and filter fixed while marker size changes
15

## Slide 15
CURRENT QUEST RUNTIME
The complete CPR acceptance test
1
Safety
2
Response
3
Call 112
4
Breathing
5
Compress
6
AED
7
Resume
8
Handover
Quest tracking must remain usable throughout the sequence
Acceptance: no random fly-in • correct orientation • acceptable wobble • loss recovery • real mannequin movement retained
Scenario 1 // Lernplattform • medical content must be approved by the project medical partners
16

## Slide 16
CURRENT QUEST RUNTIME
From technical prototype to NaReT deliverable
CONTENT
German + Polish Productive vs receptive phrases Audio + pronunciation AED and Situation B
QUALITY
Usability + accessibility Phone/tablet/desktop Privacy decisions Reliable Quest tracking
EVIDENCE
Structured user tests Quantitative + qualitative evaluation Iterative corrections Project documentation
Current Drive priorities: platform skeleton • language minigames • privacy • audio/speech • AED scope • Situation B • responsive UI • documentation
Source: NaReT Action Items board (read-only GitHub export) • JEMS A1.5 and A1.7
17

## Slide 17
CURRENT QUEST RUNTIME
How a re-anchor happens - the exact chain
17
1. Every detection produces one fused, floor-locked pose.
2. The window of the last 5 poses keeps a running MEDOID - one real measured pose, the most central. This measurement target is the markers' pure, unfiltered opinion: no dead zone, no smoothing, no prior.
3. SETTLED test: the last 3 consecutive targets must all agree within 1.5 mm / 1.0° of the newest one - movement has provably stopped.
4. DISTANCE test: the settled target must lie beyond 40 mm / 3° from the remembered rest - too far to be viewpoint bias.
5. Both passed → the newest medoid target becomes the new rest, copied verbatim. Position and rotation re-anchor independently, once per detection.
What the new rest deliberately is NOT: not the displayed pose (it contains smoothing and prior feedback - learning from it would be a feedback loop); not a single raw detection (glitch risk); not an average of the settled window (only one real measured pose is ever adopted).
navel_provider.gd::reanchor_rest_from_stable_target • SimplePoseStabilizer.measurement_target()

## Slide 18
CURRENT QUEST RUNTIME
How each value was selected - the grid method
18
INPUT - one labelled session (2026-09-04): calibration sweep, six stationary viewpoints, one measured 617.5 mm A→B→A move.
STARTUP REST - every start/step/threshold/checks/fallback combination is replayed on sliding trials of the recordings. Hard gates: ≥95% of stationary trials must confirm and ≤5% of moving trials may falsely confirm. Survivors ranked by error against the reference pose and by confirmation speed. → 30 / step 3 / 1.5 mm / 1.0° / 4 checks / fallback 100.
DISPLAY FILTER - two coordinate-descent passes over the groups (window+radius, dead zones+smoothing, prior, endpoint+re-anchor floor, timeout): every candidate is replayed end-to-end and scored half on stationary stability (wobble, jump, drift vs raw) and half on movement (amplitude retained, delay, endpoint error, return error). → window 5 • radius 0.20 m • 20 mm / 0.3° • 1.2 s • 2 s • 40 mm / 3°.
WINNER VALIDATION - movement retained 99.7% • endpoint error 4.8 mm • return error 10.4 mm.
WEAK EVIDENCE REMAINS - tracking timeout (needs a labelled loss recording) and the 10-30 mm small-move band (the session contained only one large move).
tune_filter.py • winner in tune_filter_best.txt • every evaluated configuration in tune_filter_results.csv